## Slide 1: xHCI USB3 Debug Port
Intel Open Source Technology Center
Lu Baolu
2015/09

## Slide 2: Agenda
  What is USB3 debug port?
  Why is it needed?
  Debug topology
  Operation model
  Register interface
  Software stack
  Port multiplexing
  USE CASE: early printk
  USE CASE: kgdb
  Reference

## Slide 3: What is USB3 debug port
  Optional xHCI feature defined in 7.6 of xHCI specification
  Independent of the xHCI host interface
  Debug device fully compliant with USB framework
  Provide the equivalent of a very high performance full-duplex serial link
  Only works with USB super speed.

## Slide 4: Agenda
  What is USB3 debug port?
  Why is it needed?
  Debug topology
  Operation model
  Register interface
  Software stack
  Port multiplexing
  USE CASE: early printk
  USE CASE: kgdb
  Reference

## Slide 5: Why is it needed?
  PC2001 System Design Guide requires debug capabilities in all system
  Low cost solution for legacy free debugging
  Good alternative for serial port
  10x higher data rate than USB2 debug port

## Slide 6: Agenda
  What is USB3 debug port?
  Why is it needed?
  Debug topology
  Operation model
  Register interface
  Software stack
  Port multiplexing
  USE CASE: early printk
  USE CASE: kgdb
  Reference

## Slide 7: Debug topology
Debug Target: System Under Test
Debug Host: Debug Target enumerates as USB debug device to the Debug Host, allowing a Debug Host to access a Debug Target through the standard USB software stack.
Multiple Debug Targets may be attached to a single Debug Host.
A Debug Target may only connect to a Debug Host through a Root Hub port of the target.

## Slide 8: Agenda
  What is USB3 debug port?
  Why is it needed?
  Debug topology
  Operation model
  Register interface
  Software stack
  Port multiplexing
  USE CASE: early printk
  USE CASE: kgdb
  Reference

## Slide 9: Operational model
  Bulk In/Out transfers:
    Software prepares a TRB (transfer request buffer contains pointer to DMA buffer and some control fields) in the head of the transfer ring.
    Software ring the endpoint door bell.
    Hardware schedules the transfer over USB.
    Hardware prepares a TRB in the head of the event ring.
    Software check the head of event ring periodically until seeing the completion TRB.
  Control transfers:
    Hardware takes the responsibility to handle all control transfer requests sending from the debug host.
    xHCI spec defines bits in register interface so that software knows the status or result of control transfers.

## Slide 10: Agenda
  What is USB3 debug port?
  Why is it needed?
  Debug topology
  Operation model
  Register interface
  Software stack
  Port multiplexing
  USE CASE: early printk
  USE CASE: kgdb
  Reference

## Slide 11: Register interface
Door bell
Event ring management
Control and status
Port management
Endpoint management
Device descriptor Information

## Slide 12: Agenda
  What is USB3 debug port?
  Why is it needed?
  Debug topology
  Operation model
  Register interface
  Software stack
  Port multiplexing
  USE CASE: early printk
  USE CASE: kgdb
  Reference

## Slide 13: Software stack
Linux lacks of “Debug Capability Driver” in this block.
Debug capability driver manages debug capability hardware through register interface.
Debug capability driver provides ops like read(), write() and control() to upper level debug hooks.

## Slide 14: Agenda
  What is USB3 debug port?
  Why is it needed?
  Debug topology
  Operation model
  Register interface
  Software stack
  Port multiplexing
  USE CASE: early printk
  USE CASE: kgdb
  Reference

## Slide 15: Port multiplexing
A debug port is always multiplexed with the first xHCI root hub port.
The root hub port is assigned to the debug capability and operating in an upstream facing mode when debug capability is enabled.
When root hub port is assigned to the debug capability, it appears through the xHCI as a fully functional root hub port that never sees a device attach.

## Slide 16: Agenda
  What is USB3 debug port?
  Why is it needed?
  Debug topology
  Operation model
  Register interface
  Software stack
  Port multiplexing
  USE CASE: early printk
  USE CASE: kgdb
  Reference

## Slide 17: USE CASE: early printk
  Check whether debug capability is supported.
  # cat /sys/kernel/debug/usb/xhci/<pci_bus_name>/extcap
  ...
  @ffffc90001c88700 0a USB Debug Capability
  ...
  Enable the following kernel configure options on debug target:
  CONFIG_EARLY_PRINTK
  CONFIG_EARLY_PRINTK_XDBC
  Enable the following kernel configure options on debug host:
  CONFIG_USB_SERIAL
  CONFIG_USB_SERIAL_DEBUG
  Start minicom and press Y as soon as debug target is enumerated.

## Slide 18: USE CASE: early printk
  This feature is targeted to v4.4.

## Slide 19: Agenda
  What is USB3 debug port?
  Why is it needed?
  Debug topology
  Operation model
  Register interface
  Software stack
  Port multiplexing
  USE CASE: early printk
  USE CASE: kgdb
  Reference

## Slide 20: USE CASE: kgdb
Any system debugger could be hooked to DbC.

## Slide 21: Reference
eXtensible Host Controller Interface for Universal Serial Bus http://www.intel.com/content/dam/www/public/us/en/documents/technical-specifications/extensible-host-controler-interface-usb-xhci.pdf
http://www.coreboot.org/EHCI_Debug_Port
http://composter.com.ua/documents/USB-2.0-Debug-Port%28John-Keys%29.pdf

## Slide 22
Thank you!